## Slide 1: Digital Logic Design Experiment
Haifeng Liu
haifengliu@zju.edu.cn
  http://10.71.45.100/
2016.09
Exp10. Principle and Design of Latch and Flip-flop

## Slide 2: Outline
Experiment Purpose
Instruments and Materials
Experiment Task
Experiment Principle
Content and Steps

## Slide 3: Experiment Purpose
Master composing condition and principle of latch and flip-flop
Master the difference between latches and flip-flops
Master the basic functions of SR latch, gated SR latch, D latch, SR latch, D flip-flop
Master the existing timing problem of basic SR latch, gated SR latch, D latch, SR latch, D flip-flop

## Slide 4: Instruments and Materials
Experiment Instruments
  PC with ISE 14.7 1
  SWORD Board 1
Experiment Materials
  None

## Slide 5: Experiment Task
Realize basic SR latch, and verify function and timing problems
Realize gated SR latch, and verify function and timing problems
Realize D latch, and verify function and timing problems
Realize SR master-slave flip-flop, and verify function and timing problems
Realize D flip-flop, and verify function

## Slide 6: Experiment Principle
Sufficient conditions to compose a latch
  Maintain long-term stability of a given state
  It has two stable states: 0,1
  Under certain conditions it can change logic state at any time , namely: set or set to 0
The most basic latch: SR Latch, D Latch
Latch has two stable states, known as bistable circuit

## Slide 7: SR Latch (1)
Cross link input and output of two input inverting logic device, the other input as the external information output terminal, it constitutes the most simple SR latch.
R S | Q Q | 
0 0 | Q Q | Hold
0 1 | 1 0 | Set 1
1 0 | 0 1 | Reset 0
1 1 | 0 0 | Undefined
SR Latch
SR Latch

## Slide 8: SR Latch (2)
R S | Q Q | 
0 0 | 1 1 | Undefined
0 1 | 0 1 | Reset 0
1 0 | 1 1 | Set 1
1 1 | Q Q | Hold
SR Latch
SR Latch

## Slide 9: Simulation
R=1;S=1; #50;
R=1;S=0; #50;
R=1;S=1; #50;
R=0;S=1; #50;
R=1;S=1; #50;
R=0;S=0; #50;
R=1;S=1; #50;

## Slide 10: gated SR latch
C R S | Q Q | 
0×× | Q Q | Hold
1 0 0 | Q Q | Hold
1 0 1 | 1 0 | Set 1
1 1 0 | 0 1 | Reset 0
1 1 1 | 1 1 | Undefined
SR Latch
SR Latch

## Slide 11: Simulation
C=1;R=1;S=1; #50;
R=1;S=0; #50;
R=1;S=1; #50;
R=0;S=1; #50;
R=1;S=1; #50;
R=0;S=0; #50;
R=1;S=1; #50;
C=0;R=1;S=1; #50;
R=1;S=0; #50;
R=1;S=1; #50;
R=0;S=1; #50;
R=1;S=1; #50;
R=0;S=0; #50;
R=1;S=1; #50;

## Slide 12: D Latch
The basic RS latch disadvantage: has uncertain status
Solution: Eliminate uncertain state
Just one data input terminal D
Output Q is equal to the input terminal D
Use Level to control C
C D | Q Q | 
0 × | Q Q | Hold
1 0 | 0 1 | Reset 0
1 1 | 1 0 | Set 1
D Latch
D Latch

## Slide 13: Simulation
C=1;D=1; #50;
D=0; #50;
C=0;D=1; #50;
D=0

## Slide 14: flip-flop
The disadvantage D latch: exists data flip——If the D latch directly put in sequential circuit as a state storage elements, when the enable control signal is valid, the component will lead to the internal state value change many times, rather than remain original state value
Solution: Eliminate flip, each trigger the internal state of the latch change only once
Trigger(n.): A transient state that external input enable latch state change.
Trigger(v.)：The latch circuit (bistable) that on the basis of latch while each trigger only one change of state.

## Slide 15: flip-flop
flip-flop
Master–slave
flip-flop
Edge-triggered flip-flop
Use DC feedback theory (Maintain blocking)
Use different delay time of internal circuit
Use two latches, the master latch receives input data under pulse control while the slave latch changes state and hold after the end of the pulse.
when clock edge rising or falling the state change, other time hold
Common flip-flop: Master–slave SR flip-flop, D flip-flop, JK flip-flop, T flip-flop

## Slide 16: SR master-slave flip-flop
C
S
R
Q
Q
C
R
Q
Q
C
S
R
Q
S
Q
Comprised by two clock-controlled S-R latch series, the second latch's clock is inverted.
When C = 1, the input signal into the first latch (master latch)
When C = 0, the second latch (slave latch) change the output
The path from input to output is disconnect by different clock signal value (C = 1 and C = 0)

## Slide 17: Simulation
initial begin
R=1;S=1; #50;
R=1;S=0; #50;
R=1;S=1; #50;
R=0;S=1; #50;
R=1;S=1; #50;
R=0;S=0; #50;
R=1;S=1; #50;
end
always begin
C=0;#20;
C=1;#20;
end

## Slide 18: Positive edge maintain Obstructive D flip-flop
异步控制 |  | 上升沿触发 |  |  | 
R | S | CP | D | Q | Q
0 | 1 | × | × | 0 | 1
1 | 0 | × | × | 1 | 0
1 | 1 | ↑ | 0 | 0 | 1
1 | 1 | ↑ | 1 | 1 | 0

## Slide 19: Simulation
initial begin
D = 0; #150;
D = 1; #150;
end
always begin
C=0; #50;
C=1; #50;
end

## Slide 20: Experiment Content and Step
Realize basic SR latch, and verify function and timing problems
Realize gated SR latch, and verify function and timing problems
Realize D latch, and verify function and timing problems
Realize SR master-slave flip-flop, and verify function and timing problems
Realize D flip-flop, and verify function

## Slide 21: Basic SR Latch
New project MyLATCHS
New source file SR_LATCH.sch
Use schematic diagram to design
Use NAND2 to realize
Simulation

## Slide 22: Gated SR Latch
New source file CSR_LATCH.sch
Use schematic diagram to design
Use NAND2 to realize
Simulation (include flip)
Generate symbols CSR_LATCH.sym

## Slide 23: D Latch
New source file D_LATCH.sch
Use schematic diagram to design
Use NAND2 to realize
Simulation (include flip)

## Slide 24: SR master-slave flip-flop
New source file MS_FLIPFLOP.sch
Use schematic diagram to design
invoke the CSR_LATCH
Simulation (include One-time sampling)

## Slide 25: D flip-flop
New source file D_FLIPFLOP.sch
Use schematic diagram to design
Use NAND3 to realize
Simulation

## Slide 26
Thank You !